## Slide 1
Solder Reflow Oven Using PIC18F4550
By Ahmad Mujtba & Hamza Saleem Barg
Ghulam Ishaq Khan Institute of Engineering Sciences and Technology

## Slide 2
System Block Diagram
Microcontroller
PIC18F4550 controls all operations
Temperature Sensing
MAX6675 reads thermocouple data via SPI
Output Control
PWM drives heater & fan via MOSFETs
User Interface
LCD shows temperature and setpoints

## Slide 3
Temperature vs Time Curve
Reflow Profile Phases
Preheat: gradual temperature rise
Soak: temperature stabilization
Reflow: peak temperature for soldering
Cooling: controlled temperature decrease
Key Details
Setpoint updates every 5 seconds
Follows industry-standard thermal curve
Maintains temperature with minimal overshoot

## Slide 4
System Overview
PID Temperature Control
Accurately maintains profile setpoints
Temperature Sensing
MAX6675 thermocouple amplifier via SPI
Actuation
Heater/fan driven with PWM and MOSFETs
Data & UI
LCD output and UART streaming to PC

## Slide 5
PID Control Logic
Error Calculation
Difference between setpoint and current temperature
PID Terms
Proportional: immediate response
Integral: corrects cumulative error
Derivative: predicts trend
Output
PWM scaled to 8-bit, drives heater or fan
Direction
Positive error activates heater, negative activates fan

## Slide 6
Hardware Components
PIC18F4550
Main microcontroller for control
MAX6675
Thermocouple amplifier and ADC
IRF450N MOSFETs
Switch heater & fan loads
16x2 LCD
User interface display

## Slide 7
Results Summary
Temperature Tracking
Low overshoot, accurate profile adherence
Smooth PID Adjustment
Effective PWM modulation for control
Real-time Visualization
Data streamed live via UART to PC
Validation
Verified in Proteus simulation and hardware